## Slide 1: IFAS
Integrated Flood Analysis System
Distributed by ICHARM (PWRI – JAPAN) since 2009
Rainfall – Runoff Model (Hydrological Model)
3 Versions
IFAS 1.2
IFAS 1.3
IFAS 2.0 (latest June 2014)

## Slide 2: IFAS

## Slide 3: IFAS
Input
Elevation Data (DEM)
Land Use Data
Rainfall Data
Basin Data

## Slide 4: IFAS
Condition
Project Information Manager
Basin Data Manager
Rainfall Data Manager
Parameter Manager
Dam Control Manager
Simulation Manager
Result Viewer
KML Exporter
Input
Simulation and Output

## Slide 5: Project Information Manager
X.90 | ละติจูด | ลองจิจูด
มุมล่างซ้าย | 6 deg, 25 min | 100 deg, 10 min
มุมบนขวา | 7 deg, 0 min | 100 deg, 40 min
Cell Size 1 ตารางกิโลเมตร
Start-End Date, Time
- hourly (0 h – _ h)
- daily (0 h – 23 h)
Time Interval
- hourly 60 minute
- daily 1,440 minute

## Slide 6: Project Information Manager
Target Elevation
- GlobalMap (Elevation)
Land Use
- GlobalMap (Land Cover)

## Slide 7: Basin Data Manager

## Slide 8: Basin Data Manager

## Slide 9: Rainfall Data Manager
Satellite Rainfall
GSMaP (0.1 degree = 10 x 10 km)
Past time – GSMaP MVK
Present – GSMaP NRT
TRMM (0.25 degree = 25 x 25 km)
Past time – 3B42RT V5
Present – 3B42RT V6
Ground-based Rainfall
CSV File
Thiessen Method
Time Difference
Download
Import
Edit

## Slide 10: Parameter Manager
3 Parameter Set
- Surface Parameter (Surface Tank)
- Aquifer Parameter (Groundwater Tank)
- River Course Parameter (River Course Tank)

## Slide 11: Parameter Manager

## Slide 12: Parameter Manager
Surface Parameter
No | Parameter | Definition | Unit
1 | SKF | Final infiltration capacity | cm/s
2 | HFMXD | Maximum Storage height | m
3 | HFMND | Rapid intermediate flow Height where occurs | m
4 | HFOD | Height where ground infiltration occurs | m
5 | SNF | Surface roughness coefficient | m-1/3/s
6 | FALFX | Rapid intermediate flow Regulation coefficient | 
7 | HIFD | Initial storage height | m
 | ป่าไม้
 | ไม้พุ่ม ต้นไม้ประปราย
 | เกษตรกรรม
 | ที่อยู่อาศัย
 | แหล่งน้ำ
HFMXD > HFMND > HFOD

## Slide 13: Parameter Manager
Aquifer Parameter
No | Parameter | Definition | Unit
1 | AUD | Slow intermediate flow Regulation coefficient | (1/mm/day)1/2
2 | AGD | Base flow coefficient | 1/day
3 | HCGD | Storage height where the slow intermediate flow occurs | m
4 | HIGD | Initial storage height | m
HCGD ≥ HIGD

## Slide 14: Parameter Manager
River Course Parameter
No | Parameter | Definition | Unit
1 | RBW | Constant of the Resume Law: c | 
2 | RBS | Constant of the Resume Law: s | 
3 | RNS | Manning’s roughness coefficient | m-1/3/s
4 | RRID | Initial water table of river channel | m
5 | RGWD | Infiltration of aquifer tank | 1/day
6-10 |  | Coefficient of cross shape | 
 | Range 3-4
 | Range 5-64
 | > 65
Number of cell type

## Slide 15: Dam Control Manager
4 Method
- Fixed Rate
- Fixed Value
- Fixed Rate and Fix Value
- Other Method

## Slide 16: Simulation Manager
จับคู่ข้อมูลน้ำฝนกับค่า parameter เพื่อสร้างแบบจำลอง (1 คู่ / simulation)
การ calibrate ให้ปรับที่ค่า parameter

## Slide 17: Result Viewer

## Slide 18: Result Viewer